## Slide 1: THINGS THAT STILL NEED FIXING
DATE ON TITLE SLIDE
Subtitle for new wrinkles due to shaping
BD slide (keep?) better word for unsorted fluctuations than bulk

## Slide 2: Investigation of MHD mode Structure in Shaped HBT-EP Plasmas
Patrick Byrne
Date TBD
Thesis Proposal Presentation

## Slide 3: Outline
Introduction
  Motivation for Shaped Plasma Research on HBT-EP
  HBT-EP Baseline and New Capabilities
  Analysis Procedures
New Challenges
  Plasma/Sensor coupling
  Positional Instability
Proposed Research Plan
  Observe structure and dynamics of RWM in shaped Plasmas
    Natural structure/growth rates
    RMP Response
Initial Results
Summary

## Slide 4: Outline
Introduction
  Motivation for Shaped Plasma Research on HBT-EP
  HBT-EP Baseline and New Capabilities
  Analysis Procedures
New Challenges
  Plasma/Sensor coupling
  Positional Instability
Proposed Research Plan
  Observe structure and dynamics of RWM in shaped Plasmas
    Natural structure/growth rates
    RMP Response
Initial Results
Summary

## Slide 5: Introduction - Motivation
Any fusion plasma will need to be shaped
  Fusion plasma heat load too high for material limiter
  Exhaust redirected to diverter protects instruments, VV wall
  Shaping allows access to higher β regimes, easier access to H-Mode
All present and planned advanced tokamaks are non-circular
Notes: Shaping has been shown or predicted to reduce severity of many plasma instabilities (ELMs, ITG, Sawteeth)

## Slide 6: Introduction - Motivation
Any fusion plasma will need to be shaped
HBT-EP’s Mission (in part):
  To quantify external kink dynamics and multimode response to applied magnetic perturbations… in ways that are ITER and reactor relevant[1]
Kink instabilities potentially limit performance in fusion reactors
HBT-EP is well instrumented to measure external kink modes
Shaping HBT-EP’s plasmas increases relevancy of kink studies to fusion reactors

## Slide 7: Introduction – HBT-EP Capabilities
High resolution magnetic sensors
  216 total sensors, in 3 arrays, measuring radial and poloidal field
Highly modular passively stabilizing shells
  2 independently positionable sets of 10 stainless steel/SS+ferritic walls
Active control coils
  2 coils per shell (of 6) can be independently driven for RMP or feedback

## Slide 8: Introduction – HBT-EP Capabilities
Zero-net-turns shaping coil
  Installed above inboard midplane
  Center bundle of 4 turns;
  Flanked by 2 bundles of 2
  All bundles connected in series
  Max current: 7.5 kA / turn
    Center bundle current: 2*Ip
  Arbitrary current/polarity
    Allows variety of shapes
  Fast startup, sustained current
    tstart < 1ms
    tpeak > 7ms
Notes: Peak defined as Ish greater than 90% peak Ish

## Slide 9: Introduction – Analysis procedures
Plasma equilibria solved using TokaMac
Equilibria ideal stability modeled in DCON (edge = Ψ99.5)
Predicted sensor pickup modeled using VALEN
Actual mode measurements filtered by biorthogonal decomposition

## Slide 10: Introduction – Analysis Procedures Biorthogonal Decomposition
Biorthogonal Decomposition used to resolve coherent modes from bulk? Fluctuations
  Mathematically equivalent to singular value decomposition of matrix with columns composed of individual sensor traces
  Insensitive to errors in sensor positioning or orientation
  Requires no a priori assumption of mode basis
  Allows discrimination of modes with power ~1% of total fluctuations

## Slide 11: New Challenges
Vacuum fields designed for centered, circular plasma
Shaping displaces plasma upwards, and makes vacuum fields positionally destabilizing
Theory[2] predicts passive
stabilization of plasma position
  Growth time reduced to
  scale longer than plasma
  lifetime

## Slide 12: New Challenges
Vacuum fields designed for centered, circular plasma
Shaping displaces plasma upwards, and makes vacuum fields positionally destabilizing
Theory[2] predicts passive
stabilization of plasma position
  Growth time reduced to
  scale longer than plasma
  lifetime

## Slide 13: New Challenges
Sensor arrays designed for centered, circular plasma,
as are control coils
Coupling to plasma/mode will vary poloidally.
VALEN can be used to predict coupling at each sensor/coil
  Allows us to more accurately measure plasma modes
  Allows us to maximize resonant field vs control coil current
  Novel method, can be applied to circular plasmas as well

## Slide 14: Proposed Research
Explore structure and dynamics of RWMs in shaped geometry
  Shape and growth rates of natural modes
  Effect of passive stabilization
  Response to resonant magnetic perturbations (RMP)

## Slide 15: Proposed Research - RMPs
Determine response as corvariance between control coil current and measured response field:
Observe spectrum of response
  Do the same modes couple to the same RMP in shaped/circular plasmas?
Observe magnitude of response
  Is instability greater or less?
  Are multiple modes unstable?
Apply non-resonant RMPs

## Slide 16: The HBTEP Shaping Coil
Three serially connected cable loops
  Edge bundles counterwound
  from the central cable bundle
Central bundle has twice the number of windings for zero net turns.
Very low coupling at long distances
  Minimal interaction with other magnetics, L ~10-20µH

## Slide 17: Placement and Construction
The coil will be wound around the high-field side of HBTEP at an angle of ~25 degrees above the high field side midplane.
This setup will allow the creation of local edge effects, while leaving the bulk plasma unperturbed
Fig. 1 – Flux surfaces for a weakly and fully shaped plasma. The red circle represents the last closed flux surface of an unshaped plasma

## Slide 18: Simulations Show Diversion is Possible
15º separation between coils
Coil current ~11kA (15kA max)

## Slide 19: Outline
Magnetic Geometry
The HBTEP Shaping Coil
Control Coil Shaping
Summary

## Slide 20: HBTEP Can Already Magnetically Influence The Plasma
120 Feedback coils (3 sets of 40)

## Slide 21: HBT Control Coils
120 Feedback coils (3 sets of 40)
Can apply wide spectrum of magnetic perturbations
Can be used to excite or suppress magnetic modes, or affect the shape of magnetic surfaces

## Slide 22: Shaping Coil / Control Coil Substitution
Large control coils cover 15º toroidal angle.
If fired with equal but opposite currents, nearby fields look similar to shaping coil
Discrete approximation to shaping coil

## Slide 23: Control Coil Shaped plasmas

## Slide 24: Unshaped n=1, m=3 mode activity

## Slide 25: “Triangle” shaped n=1, m=3 mode activity

## Slide 26: “Square” shaped n=1, m=3 mode activity

## Slide 27: Summary
Fusion-relevant plasma experiments (ITER,DEMO) will have non-circular cross-section
The shaping coil will allow us to gain insight into multimode instabilities in the presence of shaping.
  Degree of shaping arbitrary, including diverted operation
Experiments have indicated significant effects for a minor degree of plasma shaping