## Slide 1: Investigation of MHD Mode Structure in Shaped HBT-EP Plasmas
Patrick Byrne
April 13th, 2015

## Slide 2: Outline
Introduction
  Motivation for Shaped Plasma Research on HBT-EP
  HBT-EP Baseline and New Capabilities
  Analysis Procedures
New Challenges with Shaped Plasmas
  Plasma/Sensor coupling
  Positional Instability
Proposed Research Plan
  Observe Structure and Dynamics of RWM in Shaped Plasmas
    Natural Structure/Growth Rates
    RMP Response
Initial Results
Summary

## Slide 3: Outline
Introduction
  Motivation for Shaped Plasma Research on HBT-EP
  HBT-EP Baseline and New Capabilities
  Analysis Procedures
New Challenges with Shaped Plasmas
  Plasma/Sensor coupling
  Positional Instability
Proposed Research Plan
  Observe Structure and Dynamics of RWM in Shaped Plasmas
    Natural Structure/Growth Rates
    RMP Response
Initial Results
Summary

## Slide 4: Introduction - Motivation
A tokamak fusion plasma will need to be shaped
  Fusion plasma heat load too high for material limiter
    Exhaust redirected to diverter protects instruments, VV wall
  Shaping allows access to higher β regimes, easier access to H-Mode
All present and planned advanced tokamaks are non-circular
Notes: Shaping has been shown or predicted to reduce severity of many plasma instabilities (ELMs, ITG, Sawteeth)

## Slide 5: Introduction - Motivation
A tokamak fusion plasma will need to be shaped
HBT-EP’s Mission (in part):
  To quantify external kink dynamics and multimode response to applied magnetic perturbations… in ways that are ITER and reactor relevant[1]
Kink instabilities potentially limit performance in fusion reactors
HBT-EP is well instrumented to measure external kink modes
  High resolution magnetic sensors
  Passive stabilization and active control through flexible configuration
Shaping HBT-EP’s plasmas increases relevancy of kink studies to fusion reactors
1HBT-EP Narrative, FY 2011-2013

## Slide 6: Introduction – HBT-EP Capabilities
High resolution magnetic sensors
  216 total sensors, in 3 arrays, measure radial and poloidal field
Highly modular passively stabilizing shells
  2 independently positionable sets of 10 stainless steel/SS+ferritic walls
Active control coils
  2 coils per shell (of 6) can be independently driven for RMP or feedback

## Slide 7: Introduction – HBT-EP Capabilities
Zero net turns
  Center bundle of 4 turns (co-Ip) flanked by 2 bundles of 2 (contra-Ip)
  All bundles connected in series
    low self/mutual inductance
    Low power supply requirements
Max current: 7.5 kA / turn
  Center bundle current: 2*Ip
Arbitrary current/polarity
  Allows variety of shapes
Fast startup, sustained current
  τstart < 1ms
  τpeak > 7ms –> Ipeak > .9 * max( Imax )
Notes: Peak defined as Ish greater than 90% peak Ish

## Slide 8: Introduction – Data Acquisition
Sensors record partially integrated signal
Integrated signal in software
Smooth equilibrium fit to data
Fluctuations separated from signal by subtracting equilibrium
Fluctuations arranged and contour plotted
  Dominant mode & frequency often visible by inspection

## Slide 9: Biorthogonal Decomposition (BD)
BD resolves coherent modes from fluctuations
  Mathematically equivalent to singular value decomposition
  Coherent traveling modes isolated from fluctuations as degenerate pairs
  Modes further broken into temporal and spatial components
  Requires no a priori assumption of mode basis
  Insensitive to errors in sensor positioning or orientation

## Slide 10: Introduction – Analysis Procedures Biorthogonal Decomposition
BD resolves coherent modes from fluctuations
  Requires no a priori assumption of mode basis
  Allows discrimination of modes with
  power ~1% of total fluctuations

## Slide 11: Introduction – Analysis Procedures
Equilibrium Reconstruction: TokaMac
Inputs:
  Direct measurements
  Empircally determined constraints
Mode Energetics and Shape: DCON
Inputs:
  TokaMac Equilibrium

## Slide 12: Introduction – Analysis Procedures
Mode Measurements: BD (previously discussed)
Experiment/Simulation Connection: VALEN
  Inputs:
    DCON modes, mode rotation speed
    HBT-EP conducting structures, sensor location/orientation

## Slide 13: Introduction – Analysis
Data Acquisition
Post Processing
TokaMac
Biorthogonal Decomposition
Fourier analysis
Theory
DCON
VALEN
m/n amplitude vs. time
Coherent modes
Comparison of Shaped/Circular
Modes

## Slide 14: Outline
Introduction
  Motivation for Shaped Plasma Research on HBT-EP
  HBT-EP Baseline and New Capabilities
  Analysis Procedures
New Challenges with Shaped Plasmas
  Plasma/Sensor coupling
  Positional Instability
Proposed Research Plan
  Observe Structure and Dynamics of RWM in Shaped Plasmas
    Natural Structure/Growth Rates
    RMP Response
Initial Results
Summary

## Slide 15: New Challenges – Plasma Sensor Coupling
Sensor arrays, control coils designed for centered, circular plasma
Coupling to shaped
plasma/mode will vary poloidally
VALEN can be used to predict coupling at each sensor/coil
  More accurate measurement of plasma modes
  Resonant field vs control coil current maximized
  Novel method, can be applied to circular plasmas as well

## Slide 16: New Challenges – Plasma Sensor Coupling
VALEN can be used to predict coupling at each sensor/coil
  More accurate measurement of plasma modes
  Requires accurate equilibrium reconstruction
  Want repeatable plasma to limit number of reconstructions

## Slide 17: New Challenges
Vacuum fields designed for centered, circular plasma
  Shaping destabilizes plasma positionally
  Theory[2] predicts passive stabilization of plasma position
    Growth time reduced to scale longer than plasma lifetime
    Shaped plasmas observed to persist for multiple ideal growth times
Shaped plasma displaced upwards
  Poloidal arrays to be used
  as up/down Rogowski
  Algorithm under development,
  will require good vacuum
  field subtraction
  VALEN modeling of eddies
2A. Fukuyama, Japanese Journal of App. Phys. Vol 14, No. 6 (1978), 871-877

## Slide 18: Outline
Introduction
  Motivation for Shaped Plasma Research on HBT-EP
  HBT-EP Baseline and New Capabilities
  Analysis Procedures
New Challenges with Shaped Plasmas
  Plasma/Sensor coupling
  Positional Instability
Proposed Research Plan
  Observe Structure and Dynamics of RWM in Shaped Plasmas
    Natural Structure/Growth Rates
    RMP Response
Initial Results
Summary

## Slide 19: Proposed Research
Explore structure and dynamics of RWMs in shaped geometry
How are the natural modes affected by shaping?
  Stability, amplitude, shape, rotation frequency, disruptivity
How is the natural multimode spectrum affected by shaping?
  Relative strengths of dominant/subdominant BD modes
    Generally n = 1 vs n = 2
How effective is passive stabilization on a shaped plasma?
How does a shaped plasma respond to RMPs?
  Changes to RFA/disruptivity?
  Changes to resonant helicity?
  Coupling to sidebands?

## Slide 20: Proposed Research – Shot Development
Ensuring diversion requires deliberate equilibrium development
  Ip, MR, VF, OH, and SH affect equilibrium and shaping degree
  MR strongly affected by all other values
    Location of plasma in chamber has implications for mode measurements
Want to develop diverted, centered, MR-steady plasma
  Diverted: represents a break from previous limited operation
  Centered: strongest possible coupling to all sensors/control coils
  MR-steady: allows use of BD across long time windows
Outboard: ease of diversion
Well centered: good coupling
MR-steady: vplasma < .5cm/ms

## Slide 21: Proposed Research – Natural Modes
Grow database of shots w/ static, diverted, well coupled equilibrium
Observe modes
  As measured by sensors & segregated by BD/Fourier analysis
  As predicted by TokaMac/DCON
Compare modes
  Computationally: Through DCON
  Experimentally: Through sensors & BD/Fourier
    Naïve – Direct comparison
    VALEN – Eliminates effects of boundary shape and position
  Look at shape, amplitude, qedge, growth rates
    Dominant mode
    Subdominant mode(s)
    Correlation between modes

## Slide 22: Proposed Research - RMPs
RMP response: covariance between control coil current and measured field:
Observe spectrum of response
  Will the same modes couple to the
  same RMP in shaped/circular plasmas?
  Will the resonse peaks be in the same
  location / the same width?
Observe magnitude of response
  Is response greater or less?
  Are multiple modes unstable?
  Is the saturated level higher or lower?
  Is the plasma more disruptive?

## Slide 23: Proposed Research – Workflow/Timeline
Develop repeatable, MR-steady,
diverted & circular equilibria (x3)
Complete Mirnov Rogowski program
Select Pickup Subtraction Algorithm
Pronounced mode activity
Low mode activity
Shells in
Observe Natural Modes
Excite modes using RMP
~1.5 weeks/equilibrium (5 total)
2 weeks
1 week
Shells out
1 week/equil.
1 week/equil.
Model Equilibria w/ TokaMac
Model modes w/ DCON
Project modes to sensors with VALEN
Look for effects on:
Natural Modes: Mode Shape, Saturated Amplitude, Growth rates
Driven Modes: Mode Response, Disruptivity, Resonant Helicity/bandwidth

## Slide 24: Outline
Introduction
  Motivation for Shaped Plasma Research on HBT-EP
  HBT-EP Baseline and New Capabilities
  Analysis Procedures
New Challenges with Shaped Plasmas
  Plasma/Sensor coupling
  Positional Instability
Proposed Research Plan
  Observe structure and dynamics of RWM in shaped Plasmas
    Natural structure/growth rates
    RMP Response
Initial Results
Summary

## Slide 25: Initial Results
Shaping Coil has been constructed and installed on HBT-EP
  Allows investigation of a wide array of shaped configurations
  Diverted operation has been demonstrated for first time in HBT-EP (Shot 85385)
Shot development in process
  Well centered, MR-steady, high Ish shots under development (Shot 89341)

## Slide 26: Initial Results
VALEN has successfully been used to connect sensor measurements to Bn at plasma surface
Discrepancy between DCON and BD reduced significantly
More work required, better equilibrium modeling and larger database

## Slide 27: Initial Results – RMP Response
3 similar shaped shots w/
m/n = 3/1 RMP applied
Data and n=1 fit to data in blue, n/m 3/1 response in red
Poloidal variation of amplitude seen, as predicted by VALEN
  Strongest coupling to RMP seen at upper midplane
  Predicted to be strongest at lower midplane
Significant phase shift seen
  Suggests poloidal spectrum not just than pure m=3

## Slide 28: Outline
Introduction
  Motivation for Shaped Plasma Research on HBT-EP
  HBT-EP Baseline and New Capabilities
  Analysis Procedures
New Challenges with Shaped Plasmas
  Plasma/Sensor coupling
  Positional Instability
Proposed Research Plan
  Observe Structure and Dynamics of RWM in Shaped Plasmas
    Natural Structure/Growth Rates
    RMP Response
Initial Results
Summary

## Slide 29: Summary
This thesis will investigate:
  A novel method for projecting the output of MHD codes to predictions of direct measurements using VALEN
  The structure of resistive wall modes as the plasma boundary is shaped in various ways, including full diversion
  The growth rate and disruptivity of these modes as compared to circular plasmas
  The effect of passive stabilization on shaped plasma RWMs
  The response of shaped plasma RWMs to RMPs

## Slide 30: Introduction – Analysis procedures
Plasma equilibria solved for using TokaMac
Equilibria ideal stability modeled in DCON (edge = Ψ99.5)
Sensor pickup forward modeled using VALEN
Actual measurements decomposed to coherent modes via biorthogonal decomposition